## Slide 1: TOPOGRAPHIC MAPPING OF SURFACE WATER DRAINAGE PATTERN AND HYDROLOGICAL CONNECTIVITY ON THE CANADIAN SHIELD
Nimisha A. Wagle1, Laurence C. Smith1, Jessica V. Fayne2
1Brown University
2UCLA
ABoVE Science Team Meeting #8
May 11-M, 2022
Funded by the NASA Terrestrial Hydrology Program grant 80NSSC20K0429

## Slide 2: Why study the surface drainage pattern of the Canadian Shield?
World’s highest lake density and many topographic depressions
Projected future wetter conditions may alter surface drainage pattern and increase hydrological connectivity
Overarching Research Question:
How may a future, wetter Arctic climate affect the surface drainage pattern of the Canadian Shield?
Lake area density map
Source: Messager et. al, 2016

## Slide 3: Fill-and-Spill hydrology
Canadian shield surface hydrology relies on “fill-and-spill” (Spence and Woo, 2003; 2006)
Fill-and-spill hydrology is a critical control on downstream flow patterns and river discharge

## Slide 4: Fill-and-Spill hydrology
Canadian shield surface hydrology relies on “fill-and-spill” (Spence and Woo, 2003; 2006)
Fill-and-spill hydrology is a critical control on downstream flow patterns and river discharge

## Slide 5: Fill-and-Spill hydrology
Canadian shield surface hydrology relies on “fill-and-spill” (Spence and Woo, 2003; 2006)
Fill-and-spill hydrology is a critical control on downstream flow patterns and river discharge

## Slide 6: Fill-and-Spill hydrology
Canadian shield surface hydrology relies on “fill-and-spill” (Spence and Woo, 2003; 2006)
Fill-and-spill hydrology is a critical control on downstream flow patterns and river discharge

## Slide 7: Fill-and-Spill hydrology
Canadian shield surface hydrology relies on “fill-and-spill” (Spence and Woo, 2003; 2006)
Fill-and-spill hydrology is a critical control on downstream flow patterns and river discharge

## Slide 8: Initial work area: Baker Creek, N.W.T.
Located in the sub-Arctic Canadian Shield near Yellowknife, N.W.T.
Fill-and spill hydrology is well documented (e.g. Spence and Woo, 2003; 2006; Spence, 2018)
Well-imaged by high resolution DEMs (ArcticDEM)
Notes: Large changes in topography, vegetation, winter snow accumulation, local hydrology and surficial geology over short distances result in abrupt transitions from permafrost to non-permafrost conditions.

## Slide 9: Methodology and data
Methods
Methods
Subtract filled ArcticDEM from Original ArcticDEM
Map drainage patterns for different inundation depths using least cost path
Determine relationship between landscape scale depression storage and assumed inundation depth
Depression storage

## Slide 10: Methodology and data
Methods
Drainage pattern
Subtract filled ArcticDEM from Original ArcticDEM
Map drainage patterns for different inundation depths using least cost path
Determine relationship between landscape scale depression storage and assumed inundation depth

## Slide 11: Results:
Inundation = +10 cm

## Slide 12: Results:
Inundation = +20 cm

## Slide 13: Results:
Inundation = +30 cm

## Slide 14: Results:
Inundation = +50 cm

## Slide 15: Results:
Inundation = +100 cm

## Slide 16: Depression storage volumes and surface areas for different assumed inundation depths
Chart: Inundation depth (cm)
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 110 | 115 | 120 | 125 | 130 | 135 | 165 | 195 | 200
filled Depression Storage | 3028549.9828 | 13074814.5601 | 21607786.3821 | 20130803.9863 | 15725661.0005 | 13022387.038 | 5121472.4631 | 4551604.2147 | 4872121.6164 | 4963903.2087 | 1821606.2426 | 944284.6105 | 4127645.8021 | 3463117.4601 | 1322244.8084 | 655299.9698 | 952285.4067 | 48853945.0618 | 417314.6581 | 366530.0363 | 3887108.2053 | 307105.8947 | 8460.7575 | 8533.1143 | 4146476.3895 | 129367.5609 | 2654293.8641 | 178702.3297 | 733158.1547
cumulative Depression Storage (%) | 1.6725 | 8.8931 | 20.8261 | 31.9434 | 40.6279 | 47.8195 | 50.6479 | 53.1615 | 55.8522 | 58.5935 | 59.5995 | 60.121 | 62.4005 | 64.313 | 65.0432 | 65.4051 | 65.931 | 92.9107 | 93.1412 | 93.3436 | 95.4903 | 95.6599 | 95.6645 | 95.6692 | 97.9591 | 98.0306 | 99.4964 | 99.5951 | 100
Chart: Inundation depth (cm)
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 110 | 115 | 120 | 125 | 130 | 135 | 165 | 195 | 200
filled surface area | 8582928 | 23317296 | 33007184 | 23477188 | 15132972 | 9301928 | 3509908 | 3283400 | 3085840 | 2601920 | 1055440 | 549952 | 1810292 | 1389296 | 583248 | 375944 | 242396 | 17103216 | 159448 | 128660 | 719140 | 29052 | 3440 | 3732 | 1780940 | 53308 | 810248 | 21388 | 76380
cumulative filled surface area (%) | 5.6394 | 20.96 | 42.6472 | 58.0728 | 68.0159 | 74.1277 | 76.4339 | 78.5912 | 80.6188 | 82.3284 | 83.0218 | 83.3832 | 84.5726 | 85.4855 | 85.8687 | 86.1157 | 86.275 | 97.5126 | 97.6174 | 97.7019 | 98.1744 | 98.1935 | 98.1958 | 98.1982 | 99.3684 | 99.4034 | 99.9358 | 99.9498 | 100
Depression storage largely filled by~50 cm

## Slide 17: Hydrological connectivity increases with inundation depth
Chart: Inundation depth (cm)
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 110 | 115 | 120 | 125 | 130 | 135 | 165 | 195 | 200
Count | 174 | 286 | 231 | 144 | 131 | 68 | 43 | 34 | 17 | 19 | 10 | 7 | 11 | 6 | 8 | 4 | 3 | 5 | 3 | 3 | 1 | 2 | 1 | 1 | 1 | 1 | 3 | 1 | 1
Lake connectivity largely complete by~50 cm

## Slide 18: Conclusions
Surface water drainage pattern of the Canadian Shield can be readily modelled using high resolution DEMs
Just ~20 cm increase in regional water balance would cause a 70 percent increase in the number of Baker Creek’s topographic depressions experiencing fill-and-spill hydrology. The number of interconnected lakes would increase by 835 (+70%)
A ~50 cm increase in regional water balance would cause almost 100 percent increase in the number of Baker Creek’s topographic depressions experiencing fill-and-spill hydrology. The number of interconnected lakes would increase by 1189 (+99%)
Many new streams would be formed but the overall drainage pattern is stable (up to +1 m inundation depth)
We conclude that Canadian Shield surface water depression storage and hydrological connectivity is highly sensitive to future changes in regional water balance
Future work will explore the potential sensitivity of CS drainage patterns to changing future water balance as projected by regional climate models
Funded by the NASA Terrestrial Hydrology Program grant 80NSSC20K0429
for questions contact nimisha_wagle@brown.edu