## Slide 1
Fire & Insect Disturbance Working Group
ASTM7 Presented May 11, 2021
Photo by L Kendig
Nancy HF French, Lead
with
Laura Bourgeau-Chavez, Tatiana Loboda, Liza Jenkins

## Slide 2
Fire & Insect Disturbance Working Group
ASTM7 Presented May 11, 2021
Photo by L Kendig
Nancy HF French, Lead
with
Laura Bourgeau-Chavez, Tatiana Loboda, Liza Jenkins
Working Group Members:
Alonzo, Michael
Baltzer, Jennifer
Bourgeau-Chavez, Laura
Bouskill, Nicholas (Nick)
Chasmer, Laura
Chatterjee,
Chen, Dong
Ebel, Brian
Erb, Angela
Falkowski, Michael (Mike)
Foster, Adrianna
Genet, Helene
Goetz, Scott
Griffith, Peter
Hahn, Micah
Hall, Ella
Houben, Adam
Howard, Brian
Hoy, Elizabeth (Liz)
Jandt, Randi
Jenkins, Liza
Johnstone, Jill
Kane, Evan
Keppel-Aleks, Gretchen
Loboda, Tatiana
Mekonnen, Zelalem
Michaelides, Roger
Miller, Charles (Chip)
Natali, Susan (Sue)
Olefeldt, David
Potter, Christopher
Poulter, Benjamin (Ben)
Riley, William (Bill)
Rocha, Adrian
Rogers, Brendan
Roland, Carl
Schaefer, Kevin
Stehn, Sarah
Stofferahn, Eric
Thompson, Dan
Turetsky, Merritt
Uhelski, Dominic
Veraverbeke, Sander
Virkkala, Anna-Maria (Anna)
Walker, Xanthe
Zhang, Zhen
Previous Lead: Michelle Mack

## Slide 3: The Fire Continuum
Pre-Fire
Active Fire
Post-Fire
Active Fire
Post-Fire
Pre-Fire
Vegetation WGs
Disturbance Synthesis
Hydrology & Permafrost WG
Vegetation WGs
Crosscutting WGs:
Carbon Dynamics
Ecosystem Services
Wetlands
Snowscapes

## Slide 4: Fire and Insect Disturbance WG Report:
1. Current activities of ABoVE Investigators (published  in prep)
  9 slides from 4 projects – Investigator & PI are identified on each slide
  Additional products & outputs
  NOT detailed nor comprehensive
2. Future Plans for WG:
  Tundra Fire Synthesis
  WG logistics for participation
3. Working Group accomplishments
  Data sets
  Summary of boreal synthesis
Observations
Remote
In-situ
Modeling
Mapping
Predicting
Vulnerability
Resiliency

## Slide 5
Significance:
Results further showed that the timing of spring snowmelt has played a significant role in slowing the growth of new woody vegetation in years when there was an anomalously early snow-free date.
NASA satellite imagery has identified several large fires of special interest that can be monitored with high-resolution remote sensing to track any slowing in long-term recovery from severe burns in the ABOVE study domain
Changes in Growing Season Phenology
Following Wildfires in Alaska
Christopher Potter, NASA Ames Research Center, (June 2020)
Remote Sensing in Earth Systems Sciences 3, 95–109 (2020). doi: 10.1007/s41976-020-00038-7
Background:
Extreme fire years in Alaska, such as 2004 and 2005, have been characterized by large areas burned at high severity, disturbance events which have been attributed to climate warming trends.
The objective of this study, as part of the NASA Arctic Boreal Vulnerability Experiment (ABoVE) campaign, was to understand changes in vegetation cover for all wildfire burned areas in Alaska from 2004-2005 using the entire record of MODIS satellite greenness (Normalized Difference Vegetation Index - NDVI).
Findings:
This is the first study that has used the complete vegetation index record from MODIS in a comprehensive statewide analysis to show that the predominant vegetation cover type in most regrowing burned areas of Interior Alaska a decade post-fire is still deciduous shrub and young tree cover.
Analysis:
Monthly MODIS (Moderate Resolution Imaging Spectroradiometer) data from 2000 to 2018 was used to track total integrated greenness cover (TIN) and end of the season timing (EOST) date in “greening versus browning” vegetation change detection.
Yearly changes in MODIS vegetation metrics
by fire burn severity class
Fire Recovery C Potter
Notes: Citation: Potter, C., 2020, Changes in Growing Season Phenology Following Wildfires in Alaska, Remote Sensing in Earth Systems Sciences.
This work was supported by NASA Ames Research Center and the NASA Terrestrial Ecology program.

## Slide 6
R2 = 0.73
R2 = 0.67
R2 = 0.64
Fire Severity N French (Bourgeau-Chavez)
Field data
Develop Random Forest Model using Landsat
Map modeled severity with Landsat

## Slide 7
Wildfire combustion and carbon stocks in the southern Canadian boreal forest: Implications for a warming world
Dieleman, C. M., Rogers, B. M., Potter, S., Veraverbeke, S., Johnstone, J. F., Laflamme, J., Solvik, K., Walker, X. J., Mack, M. C. and Turetsky, M. R.: Wildfire combustion and carbon stocks in the southern Canadian boreal forest: Implications for a warming world, Global Change Biology, doi:10.1111/gcb.15158, 2020.
Background:
Wildfires in boreal forests are are increasing in frequency and emit globally significant levels of greenhouse gases to the atmosphere. Nonetheless, fire carbon emissions of the more productive and frequently burning southern Canadian boreal forests are relatively understudied.
Methods:
We sampled 47 burned and 32 unburned sites in three fire scars from the 2015 fire season.
Laboratory techniques and statistical models were used to calculate carbon stocks and combustion (i.e., carbon emissions per unit area).
We used a cross-study latitudinal synthesis to assess implications for northern boreal forests.
Remote sensing and other geospatial predictors were used in a machine learning framework to extrapolate combustion across 2015 Saskatchewan fires.
Findings:
Our field sites emitted an average of 3.3 kg C m-2 and our extrapolated model estimated an average of 2.5 kg C m-2 across 2015 Saskatchewan fires, resulting in a total of 36.3 Tg C.
Sites affected by historical timber harvesting exhibited faster recovery and larger combustion levels compared to sites recovering from fire.
Using the southern boreal as an analog, northern boreal forests may undergo fundamental shifts to younger forests storing less carbon.
Significance:
Wildfires in southern boreal forests are a critical component of the boreal carbon balance.
Timber harvest must be accounted for in regional carbon budgets, including direct and indirect effects on stand carbon dynamics and subsequent disturbances.
Northern boreal forests are at high risk of losing carbon to the atmosphere from climate change.
(years)
Combustion as a function of stand age, ecozone, and site moisture class (top), and spatially extrapolated combustion at 30 m across Saskatchewan, Canada (bottom). Note the generally higher combustion values in older stands and the Boreal Plains ecozone, corresponding to the southern and western portions of Saskatchewan.
Fire carbon emissions C Dieleman (Rogers)
Notes: Full citation: Dieleman, C. M., Rogers, B. M., Potter, S., Veraverbeke, S., Johnstone, J. F., Laflamme, J., Solvik, K., Walker, X. J., Mack, M. and Turetsky, M. R.: Wildfire combustion and carbon stocks in the southern Canadian boreal forest: Implications for a warming world, Global Change Biology
Associated data archives:
Dieleman, C., Rogers, B. M., Veraverbeke, S., Johnstone, J. F., Laflamme, J., Gelhorn, L., Solvik, K., Walker, X. J., Mack, M. C. and Turetsky, M. R.: ABoVE: Characterization of Burned and Unburned Boreal Forest Stands, SK, Canada, 2016, ORNL DAAC, doi:10.3334/ORNLDAAC/1740, 2020.
Potter, S., Rogers, B.M. and Dieleman, C.: ABoVE: Spatial Estimates of Carbon Combustion from Wildfires across SK, Canada, 2015, ORNL DAAC, doi:10.3334/ORNLDAAC/1787, 2020.
Grants: This work was funded by the National Aeronautics and Space Administration (NASA) Arctic-Boreal Vulnerability Experiment (ABoVE NNX15AU56A and NX15AT71A) managed by Hank Margolis (Rogers TE 2014 and Mack 2018 projects) and by multiple grants from the Natural Sciences and Engineering Research Council of Canada (NSERC).
Remote sensing: We used Landsat-derived fire severity (differenced Normalized Burn Ratio) and tree cover together with a suite of other geospatial predictors related to topography, fire weather, long-term climate, tree species, soil properties, stand age, and ecozones to model and map fire carbon emissions across 2015 Saskatchewan fires at 30 m.
Abstract: Boreal wildfires are increasing in intensity, extent, and frequency, potentially intensifying carbon emissions and transitioning the region from a globally significant carbon sink to a source. The productive southern boreal forests of central Canada already experience relatively high frequencies of fire, and as such may serve as an analogue of future carbon dynamics for more northern forests. Fire-carbon dynamics in southern boreal systems are relatively understudied, with limited investigation into the drivers of pre-fire carbon stocks or subsequent combustion. As part of NASA’s Arctic – Boreal Vulnerability Experiment (ABoVE), we sampled 79 stands (47 burned, 32 unburned) throughout central Saskatchewan to characterize above- and belowground carbon stocks and combustion rates in relation to historical land use, vegetation characteristics, and geophysical attributes. We found southern boreal forests emitted an average of 3.3 ± 1.1 kg C m-2 from field sites. The emissions from southern boreal stands varied as a function of stand age, fire weather conditions, ecozone, and soil moisture class. Sites affected by historical timber harvesting had greater combustion rates due to faster carbon stock recovery rates than sites recovering from wildfire events, indicating that different boreal forest land use practices can generate divergent carbon legacy effects. We estimate the 2015 fire season in Saskatchewan emitted a total of 36.3 ± 15.0 Tg C, emphasizing the importance of southern boreal fires for regional carbon budgets. Using the southern boreal as an analog, the northern boreal may undergo fundamental shifts in forest structure and carbon dynamics, becoming dominated by stands <70 years old that hold 2 – 7 kg C m-2 less than current mature northern boreal stands. Our latitudinal approach reinforces previous studies showing that northern boreal stands are at a high risk of holding less carbon under changing disturbance conditions.

## Slide 8
Widespread shrub-fire positive feedback loop in Arctic tundra
Dong Chen, Cheng Fu, Liza K. Jenkins, Jiaying He, Randi R. Jandt, Allison Baer, Tatiana V. Loboda
Through analyzing all available Landsat imagery and field data that we collected in Noatak and Seward Peninsula, we show that a shrub-fire feedback loop widely exists across Alaskan tundra
  Wildfires lead to higher shrub presences for decades after the fires
  More severe wildfires lead to higher levels of shrubification
  Elevated shrub levels for decades before wildfires occurred
There are considerable spatial variations in shrub-fire relationships across Alaskan tundra, which are attributable in part to differences in species composition and biomass
This study confirms, for the first time at the regional level, that a domain-wide shrubification process is underway in Alaskan tundra.
Manuscript in Review
Shrub-Fire Feedbacks D Chen (Loboda)

## Slide 9: Intersection of Organic Layer (Peat) Severity Map with Ecotype Map
Fire Disturbance/Regrowth Modeling Bourgeau-Chavez
Wet ECOTYPE Dry
Treed peatlands are burning more area than expected in the early season and on the Plain in 2015; but they are burning less severely than expected across the region
Wetlands (all peatlands and lowland sampled sites) are showing greater resiliency than uplands but also greater regeneration failure
Ecosystem vulnerability (Weißhuhn et al. 2018) 3 elements:
1. Exposure, which in our analysis is the probability of wildfire disturbance; HIGH
2. Sensitivity, which in this case is susceptibility to the wildfire hazard; MODERATE
3. Adaptive Capacity, which is related to resilience (i.e. is conifer self-replacing): MOSTLY but some regen failure
Two manuscripts in production on fire effects and peatland vulnerability results

## Slide 10: Modeling carbon emissions with CanFIRE
FATES-CLM-HH pre-disturbance
FATES-CLM-HH post-disturbance
O= organic layer, A= active layer, P = permafrost
Calibrate and assess FATES-CLM-HH with field and RS data.
Validate against field, RS and CanFIRE C outputs.
Fire Disturbance/Regrowth Modeling Bourgeau-Chavez
Measurements of burn severity, revegetation trajectory, active layer thickness, fuel loads biomass amounts and near surface soil moisture used to assess performance.
Paired simulations to evaluate effect of fire and assess feedbacks with vegetation and moisture conditions
Projections with future climate conditions.
Modeling interactions between hydrology & wildfire with FATES-SPITFIRE-CLM-HH
Notes: Calibrate and assess FATES-CLM-HH with field and RS data. Validate against field, RS and CanFIRE C outputs. Measurements of burn severity, revegetation trajectory, active layer thickness, fuel loads biomass amounts and near surface soil moisture used to assess performance.
Paired simulations to evaluate effect of fire and assess feedbacks with vegetation and moisture conditions
Projections with future climate conditions.

## Slide 11
Fire Disturbance/Regrowth Modeling J Shuman, A Foster (Bourgeau-Chavez)
Process-based fire simulation across model frameworks
fire weather
temperature humidity
wind speed
lightning strikes
fuel loading bulk density surface area moisture
Rate of spread & intensity
UVAFME
FATES implementing moss and active crown fire
Foster et al. in prep
UVAFME
FATES
Notes: UVAFME and FATES both handle fire behavior and effects with process-based fire simulation, with rate of spread and fire intensity based on a combination of fire weather and lightning strike frequency, and fuel loading, geometry, and moisture.
UVAFME has been validated against site level above- and below-ground combustion data across the ABoVE domain and will be used to benchmark and validate the FATES model.
Moss and active crown fire was demonstrated to be an essential component for capturing fire behavior and dynamics, and is being implemented in FATES.
UVAFME and FATES are being compared in a systematic framework using FATES forcing data to drive both models and evaluate processes similarity and difference across models.
Additional comments from email: The first slide shows that both UVAFME and FATES use similar process based fire modeling. There are differences in handling of moss and crown fire. Specifically, UVAFME has this, and FATES is implementing this. These are UVAFME comparisons against above ground combustion across the domain that Adrianna is preparing for publication. (She also has a below ground comparison that looks good.) We have the comparative framework setup for UVAFME and FATES and my talk discusses this within the modeling framework session.

## Slide 12
Fire Disturbance/Regrowth Modeling J Shuman, S Swenson (Bourgeau-Chavez)
Hillslope terrain remapping to capture moisture variability
Upland columns have variable soil moisture due to N/S aspect differences
Lowland columns are wetter with less variability than upland
Transpiration increases with solar radiation
Transpiration (QVEGT)
Soil Moisture (ZWT)
Aspect
CTSM-HH (Hillslope Hydrology) uses remapping from ABoVE 10m DEM to determine multiple hillslope columns
CTSM-HH will be used to evaluate changing fire behavior related to site variability
Soil Moisture(ZWT) vs Transpiration (QVEGT)
Solar radiation (FSDS) vs Transpiration (QVEGT)
Lowland columns
South facing
slopes
North facing
slopes
Upland columns
more moisture
less moisture
ZF17 burn site
Notes: Notes from email: The second slide presents Sean's hillslope hydrology (HH) terrain mapping based on HAND (Height above nearest drainage), elevation, slope and aspect characteristics. This is a remapping of a 25km grid cell inside the ZF17 burn (NW territories near Slave Lake) with the ABoVE 10m DEM from Scott Goetz's group to remap and capture catchments using multiple thresholds of variation to test where the catchments become important to capturing drainage. With this remapping procedure Sean classifies the landscape into representative hillslopes used in the modeling. These maps and graphs demonstrate that this classification captures variation in soil moisture and aspect (as well as other things not shown) and this translates into a response for vegetation transpiration. This is a large step forward for capturing hillslope variability in an Earth System Model (ESM) framework. We will be looking to validate this at different spatial scales (site,regional) and with various measurements (soil moisture, drainage, vegetation). Andrew Poley's drainage class map will be used as validation for this HH mapping. With the HH the aim is to capture variability in site characteristics and use that in modeling to track changes on fire behavior.

## Slide 13
Missing burns in the high northern latitudes: The case for regionally focused burned area products
Dong Chen, Allison Baer, Tatiana V. Loboda
We compared 3 existing burned area products in circumpolar boreal forests and tundra
  MCD64A1 (Giglio et al. 2009)
  ABBA (Loboda et al., 2017; https://daac.ornl.gov/ABOVE/guides/Arctic_Boreal_Burned_Area.html)
  FireCCI51 (Lizundia-Loiola et al. 2020)
Our results show that MCD64A1 has large commission error and omission error in the HNL
  But omission error dominates over commission error
MCD64A1 considerably underestimates burned areas in the HNL
  It misses about ¼ of total burned areas in HNL in North American during 2001-2015
Fire-related models based on MCD64A1 are therefore likely to substantially underestimate wildfires’ impacts in the HNL
Regional burned area products likely outperform MCD64A1 in mapping accuracy
For now, ABBA seems to be the burned area product with the highest accuracy in mapping wildfires in circumpolar HNL at MODIS-like resolutions
Manuscript in preparation
Fire Burn Area D Chen (Loboda)

## Slide 14: Related Paper
Ecosystem carbon pools and wildfire losses across successional trajectories.
  In all stands (N = 75), black spruce dominated density and biomass prior to fire.
  Assess above- and belowground C across three successional trajectories of tree regeneration.
Results:
  Shifts in dominant plant species catalyzed by severe fire compensated for greater combustion of soil carbon over decadal time scales.
  Severe burning of organic soils shifted tree dominance from slow-growing black spruce to fast-growing deciduous broadleaf trees
  Net increase in carbon storage by a factor of 5 over the disturbance cycle.
Mack et al., Science 372, 280–283 (2021) 16 April 2021
The relationship between pre- and post-fire SOL C pools for three successional trajectories of tree regeneration.

## Slide 15: WG Activity: Tundra Fire Synthesis
Current focus on this WG will be the Tundra Fire Synthesis
  Ideas stem from discussions during NAU workshop – Tundra was split off from Boreal due to the paucity of data on Tundra (at the time) compared to Boreal
  Would like to integrate remote sensing into the synthesis, in addition to field data compilation and assessment.
  Stress use of observations that allow improvement to modeling & prediction
  Climate-driven changes in Tundra fire to inform land management for ecosystem services.
Figure Courtesy of A. Rocha

## Slide 16: Potential Focus Areas for Synthesis
Ideas under discussion (from notes & survey - unfiltered):
Tundra fire combustion & regrowth (from NAU workshop)
Drivers of fire occurrence & change: lightning, climate, soil/fuel moisture (weather), shrub density
Carbon cycle & mechanisms of recovery
Fire impacts on nutrients, microbial community, climate, competition
Moisture, hydrology, permafrost interactions with fire
Post-fire impacts on permafrost (drivers, magnitude, future changes, etc.)
Effects of fire on landscape scale
Post-fire trajectories
Ecosystem succession in the tundra
2007 Anaktuvuk River tundra fire, North Slope, Alaska (Photo: U.S. Bureau of Land Management)

## Slide 17: Tundra Fire Synthesis
Logistics:
Will meet every 4 weeks to make significant initial progress. If you want to contribute, join the WG through the ABoVE website.
  Fill out “whenisgood” poll ASAP – sent to members in April (https://whenisgood.net/5g3n5ww)
Initial Tundra Fire Synthesis meeting consisted of mini-briefings from different projects/PIs
Currently working on developing the aim and boundaries of the synthesis analysis and paper
  Survey link to poll WG members
  Compiling relevant literature
Initial scoping work will culminate in a workshop
  Blended format (in-person with remote participation accommodated)
2007 Anaktuvuk River tundra fire, North Slope, Alaska (Photo: U.S. Bureau of Land Management)

## Slide 18: Synthesis Accomplishments of WG:
Title: Arctic-boreal wildfire combustion synthesis ****** 2 publications! With 1 in prep
Description: Michelle Mack and Xanthe Walker hosted a 2.5 day workshop at Northern Arizona University in May 2017. The Fire & Insect Disturbance Working Group (Previously Wildfire Disturbance WG) collected and synthesized field measurements on carbon emissions from wildfire across the ABoVE domain.
Activity Leads: Mack / Walker / Rogers / Bourgeau-Chavez
Status: Two papers published; 1 manuscript in prep
  Xanthe Walker: Frontiers in Forests and Global Change (2020) focused on differences in ecosystem structure and fire carbon emissions across ecoregions,
  Xanthe Walker: Nature Climate Change (2020) focused on the site-level drivers of combustion.
  Brendan Rogers: using the database to model and map burned area and carbon emissions across the ABoVE domain from 2001 - 2019.
Title: Boreal post-fire regeneration synthesis ****** 1 publication in review!
Description: As part of the 2.5 day workshop at NAU in 2017, a group of investigators collected and compiled post-fire regeneration data and led a subsequent synthesis on the patterns and drivers of forest resilience to disturbance.
Activity Leads: Baltzer / Day / Mack / Johnstone
Status: 1 manuscript in review
  Jennifer Baltzer submitted a manuscript to PNAS (in Dec. 2020) on the vulnerability of black spruce, and conifers more generally, to fire-induced shifts in species composition.

## Slide 19: Archived Data Sets
Data archives: 16 products archived; at least 4 submitted and being processed; several more planned (see ABoVE web site for “official” record)
Mack:
Walker, X.J., J.L. Baltzer, L.L. Bourgeau-Chavez, N.J. Day, W.J. De groot, C. Dieleman, E.E. Hoy, J.F. Johnstone, E.S. Kane, M.A. Parisien, S. Potter, B.M. Rogers, M.R. Turetsky, S. Veraverbeke, E. Whitman, and M.C. Mack. 2019. ABoVE: Synthesis of Burned and Unburned Forest Site Data, AK and Canada, 1983-2016. ORNL DAAC, Oak Ridge, Tennessee, USA. https://doi.org/10.3334/ORNLDAAC/1744
Walker, X.J., J.L. Baltzer, W. Laurier, S.G. Cumming, N.J. Day, S.J. Goetz, J.F. Johnstone, S. Potter, B.M. Rogers, E.A.G. Schuur, M.R. Turetsky, and M.C. Mack. 2019. ABoVE: Characterization of Carbon Dynamics in Burned Forest Plots, NWT, Canada, 2014. ORNL DAAC, Oak Ridge, Tennessee, USA. https://doi.org/10.3334/ORNLDAAC/1664
Walker, X.J., B.M. Rogers, J.L. Baltzer, S.R. Cummings, N.J. Day, S.J. Goetz, J.F. Johnstone, M.R. Turetsky, and M.C. Mack. 2018. ABoVE: Wildfire Carbon Emissions and Burned Plot Characteristics, NWT, CA, 2014-2016. ORNL DAAC, Oak Ridge, Tennessee, USA. https://doi.org/10.3334/ORNLDAAC/1561
Rogers:
Dieleman, C., Rogers, B. M., Veraverbeke, S., Johnstone, J. F., Laflamme, J., Gelhorn, L., Solvik, K., Walker, X. J., Mack, M. C. and Turetsky, M. R. , 2020. ABoVE: Characterization of Burned and Unburned Boreal Forest Stands, SK, Canada, 2016, ORNL DAAC, 10.3334/ORNLDAAC/1740
Potter, S., Rogers, B.M. and Dieleman, C. 2020. ABoVE: Spatial Estimates of Carbon Combustion from Wildfires across SK, Canada, 2015, ORNL DAAC, doi:10.3334/ORNLDAAC/1787
Solvik, K.K., S. Potter, A.M. Erb, M. Roman, C. Schaaf, Q. Sun, Z. Wang, and B.M. Rogers. 2019. ABoVE: MODIS-Derived Daily Mean Blue Sky Albedo for Northern North America, 2000-2017. ORNL DAAC, Oak Ridge, Tennessee, USA. 10.3334/ORNLDAAC/1605
Veraverbeke, S., B.M. Rogers, M.L. Goulden, R. Jandt, C.E. Miller, E.B. Wiggins, and J.T. Randerson. 2017. ABoVE: Ignitions, burned area and emissions of fires in AK, YT, and NWT, 2001-2015. ORNL DAAC, Oak Ridge, Tennessee, USA. https://doi.org/10.3334/ORNLDAAC/1341
Bourgeau-Chavez
Bourgeau-Chavez, L.L., S. Endres, L. Jenkins, M. Battaglia, E. Serocki, and M. Billmire. 2017. ABoVE: Burn Severity, Fire Progression, and Field Data, NWT, Canada, 2015-2016. ORNL DAAC, Oak Ridge, Tennessee, USA. https://doi.org/10.3334/ORNLDAAC/1548
Bourgeau-Chavez, L.L., N.H.F. French, S. Endres, L. Jenkins, M. Battaglia, E. Serocki, and M. Billmire. 2016. ABoVE: Burn Severity, Fire Progression, Landcover and Field Data, NWT, Canada, 2014. ORNL DAAC, Oak Ridge, Tennessee, USA. http://dx.doi.org/10.3334/ORNLDAAC/1307
Bourgeau-Chavez, L.L., M. Battaglia, E.S. Kane, L.M. Cohen, and D. Tanzer. 2019. ABoVE: Post-Fire and Unburned Vegetation Community and Field Data, NWT, Canada, 2018. ORNL DAAC, Oak Ridge, Tennessee, USA. https://doi.org/10.3334/ORNLDAAC/1703
Bourgeau-Chavez, L.L., J.A. Graham, S. Endres, N.H.F. French, M. Battaglia, D. Hansen, and D. Tanzer. 2019. ABoVE: Ecosystem Map, Great Slave Lake Area, Northwest Territories, Canada, 1997-2011. ORNL DAAC, Oak Ridge, Tennessee, USA. https://doi.org/10.3334/ORNLDAAC/1695
French, N.H.F., J.A. Graham, L.L. Bourgeau-Chavez, S. Grelick, and E. Whitman. 2020. ABoVE: Burn Severity of Soil Organic Matter, Northwest Territories, Canada, 2014-2015. ORNL DAAC, Oak Ridge, Tennessee, USA. https://doi.org/10.3334/ORNLDAAC/1694
2 additional products submitted to the DAAC with 2017 and 2019 field data
Loboda
He, J., T.V. Loboda, L. Jenkins, and D. Chen. 2019. ABoVE: Distribution Maps of Wildland Fire Fuel Components across Alaskan Tundra, 2015. ORNL DAAC, Oak Ridge, Tennessee, USA. https://doi.org/10.3334/ORNLDAAC/1761
Loboda, T.V., J.V. Hall, and A. Baer. 2017. ABoVE: Wildfire Date of Burning within Fire Scars across Alaska and Canada, 2001-2019. ORNL DAAC, Oak Ridge, Tennessee, USA. https://doi.org/10.3334/ORNLDAAC/1559
Loboda, T.V., D. Chen, J.V. Hall, and J. He. 2018. ABoVE: Landsat-derived Burn Scar dNBR across Alaska and Canada, 1985-2015. ORNL DAAC, Oak Ridge, Tennessee, USA. https://doi.org/10.3334/ORNLDAAC/1564
Loboda, T.V., J.V. Hall, A.H. Hall, and V.S. Shevade. 2017. ABoVE: Cumulative Annual Burned Area, Circumpolar High Northern Latitudes, 2001-2015. ORNL DAAC, Oak Ridge, Tennessee, USA. https://doi.org/10.3334/ORNLDAAC/1526
2 additional products submitted to the DAAC

## Slide 20
Fire & Insect Disturbance Working Group
ASTM7 Presented May 11, 2021
Photo by L Kendig
Discussion